## Slide 1
Kiosk Internet Uplink
HAT vs 4G Router
Why not the WiFi dongle · The case for and against each cellular option
Discussion draft · August 28, 2026

## Slide 2
The Decision
The kiosk needs its own internet for email intake now, and for database sync and digital-wallet payment soon. It has to work in public locations where we can't rely on venue WiFi, so the uplink has to be cellular. Two ways to add cellular: a HAT on the Pi, or a standalone 4G router the Pi plugs into. This deck lays out both to weigh.
Rule Out the Dongle
A WiFi client needs a trusted local network we won't reliably have
Two Cellular Options
SIM7600G-H HAT on the Pi, or a separate 4G router
Weigh It Together
Power, integration effort, field support, cost — no default pick yet

## Slide 3
What Rides on the Uplink
Email Submission — live now
IMAP poll + SMTP reply; a short outage is only a minor delay
SQLite -> Cloud Sync — near-term
Continuous low-bandwidth WAL shipping for remote admin
Digital-Wallet Payment — potential
Real-time QR confirm; an outage means a failed sale at the kiosk
Each feature raises the uptime bar — the uplink choice should assume always-on, with a watchdog.

## Slide 4
Ruled Out — The USB WiFi Dongle
What Was Proposed
• Cheapest option — a ~$10 USB WiFi adapter, supervisor's preference on cost
• Pi joins an existing WiFi network for its internet
Why It Doesn't Fit This Kiosk
• Deploys in varied public sites with no WiFi we control
• The school lobby's only network is faculty-restricted
• Built-in Pi radio is already the customer upload hotspot
• A dongle with nothing reliable to join is dead weight
If It Ever Comes Back
• Only as an opportunistic extra behind the cellular route
• One in-kernel MT7612U dongle, to save data where free WiFi exists — deferred

## Slide 5
Option A — SIM7600G-H 4G HAT
The Case For
• Runs off the kiosk's one existing power cable — no second plug
• One integrated unit; it's the part already in project_objectives.txt
• Roadmap Phase 5 is already designed around it (ModemInterface / SimModem)
• Global LTE bands incl. all of SEA, with 3G/2G fallback
The Case Against
• Fiddly on Linux: ModemManager, USB mode-switch, PWRKEY pulse on boot
• We build and maintain the reconnect / watchdog / modem-reset logic
• ~2A TX bursts can brown out the Pi rail — needs a stronger PSU + heatsink
• Covers the GPIO header — must confirm pass-through vs coin/bill/hopper pins

## Slide 6
Option B — Standalone 4G Router
The Case For
• Pi connects by plain DHCP over its free Ethernet port — zero modem code
• Deletes Phase 5's modem-integration workstream entirely
• Reconnect logic is the router's only job, with a diagnostics web UI
• A dead unit is an operator box-swap; no GPIO header contention
The Case Against
• Needs its own mains PSU and a second plug out of the sealed enclosure
• Or added internal power plumbing (IEC inlet + strip, or a DC-DC feed)
• A second box to mount and power inside every unit
• Diverges from the BOM; 5V models that share the Pi supply cost more

## Slide 7
Head to Head
Power & Cabling
• HAT: one PSU, one cable — the kiosk's existing feed
• Router: a second mains plug, or internal power plumbing
Pi-Side Integration
• HAT: modem bring-up + watchdog we write and maintain
• Router: none — plain Ethernet, nothing to configure
Field Support
• HAT: module fault = tech visit; config tied to the Pi image
• Router: swap the box, Pi untouched
Cost & Roadmap Fit
• HAT: ~$55 + antennas (+ maybe PSU); matches BOM and Phase 5
• Router: ~$50-60 + its own PSU; drops the modem workstream

## Slide 8
Concrete Parts — What Each Option Buys
Option A — SIM7600G-H 4G HAT build
• Waveshare SIM7600G-H 4G HAT — the part already in the BOM, ~$60-85 (Waveshare direct / Amazon); the "(B)" variant adds GNSS
• Better-supported alternative: Sixfab Base HAT + Quectel EG25-G, ~$75-100 — Sixfab's connection manager replaces watchdog/reconnect code we'd otherwise write
• Raspberry Pi 27W USB-C PSU (5.1V / 5A), ~$14 — one supply with headroom for the modem's ~2A TX bursts
• 2x SMA LTE paddle antennas (~$10), stick-on heatsink for the module, PWRKEY jumpered to a spare GPIO for boot pulse + software reset
Option B — Standalone 4G router
• Baseline: TP-Link Archer MR200 — LTE Cat-4, 4x Ethernet, web diagnostics UI, mains PSU included, ~$65-110
• Same class: Huawei B311 / B535, ~$55-80 — mains-powered, one RJ45 LAN
• Single-supply option: GL.iNet GL-XE300 "Puli" — 5V USB-C in, OpenWrt diagnostics, ~$110-130; avoids a second mains voltage but still its own cable/port
• Pi connects over its free Ethernet port by DHCP — nothing else to add on the Pi side
Either way
• Local prepaid data SIM (Globe / Smart / DITO), standard 4G APN — recurring cost already approved
• All candidate modems/routers cover PH LTE bands (B3 / B28 / B41) and the wider SEA set; confirm against the chosen carrier before ordering
• Antenna cable gland / strain relief where the lead exits the wooden enclosure

## Slide 9
Open Questions for the Group
Second Power Feed — Acceptable?
Can the enclosure take a second mains plug or an internal power strip, or is a single cable a hard constraint?
Appetite for Modem Integration
Are we comfortable owning the SIM7600 bring-up and watchdog code, given the team size?
GPIO Header Check
Confirm whether the HAT variant passes through the pins the coin/bill/hopper wiring needs.
Bench Test Before Buying
Prove stable reconnect under load on one SIM7600G-H first — the hardware isn't on the critical path yet.