## Slide 1
Kiosk QR Scanner
Engine vs Camera vs Gun
Why not the Pi camera · The case for an embedded scan engine · Recommended parts
Proposal draft · September 3, 2026

## Slide 2
The Decision
The Read
QR / OTP off a customer's phone screen — unattended, fixed-mount, indoors now
Rule Out 1D Laser
no 2D symbologies, and a laser can't read an emissive display at all
Rule Out the Pi Camera
it makes ambient light our problem forever — fails the adaptable-lighting goal
Three Options Left
Pi camera as plan B, a consumer HID gun, or an embedded scan engine
Decide On
lighting tolerance · fit into an unattended app · cost and roadmap
The Raspberry Pi 4 is already fixed in the BOM — the scanner only has to talk to it.

## Slide 3
Ruled Out — The Raspberry Pi Camera
What It Looked Like
• Pi Camera Module 3 (autofocus) + zbar / pyzbar, or OpenCV QRCodeDetector
• Smallest bill-of-materials delta — camera + ribbon, no new interface
• Familiar part; decoding 23 ASCII bytes off a screen is well-trodden
Why It Doesn't Fit
• Adds an exposure / gain / focus CV pipeline AND an OS image to maintain
• Every new site's lighting becomes a re-tuning task — the opposite of the goal
• Only pays off if the camera also does OCR or capture; here it does neither
If It Ever Comes Back
• Documented plan B only: Pi Camera Module 3 + pyzbar behind a shroud with added light
• Revisit only if a camera is needed for a separate feature

## Slide 4
Option A — Consumer 2D Imager (HID Gun)
The Case For
• Reads phone screens well out of the box — no decode software to write
• Keyboard-wedge input 'just works'; this is the class already in project_objectives.txt (LogicOwl OJ-HS-23)
• Real warranty; a dead unit is a two-minute plug swap
The Case Against
• A bulky external gun to mount and shroud on a fixed kiosk face
• HID keyboard-wedge depends on window focus and an input layer — fragile in an unattended Qt app
• Little control over beep, trigger mode, or re-read timing

## Slide 5
Option B — Embedded 2D Scan Engine (USB-CDC Serial)
The Case For
• Same decode silicon as the consumer guns, in a module built to sit behind a kiosk window
• Own aimer + active illumination — consistent reads as ambient light changes
• Virtual serial device: newline-delimited 'sid:otp' from /dev/ttyACM0, no focus / X dependency
• Full control of trigger mode, beep, and re-read delay via setup barcodes
The Case Against
• We write a small serial-reader manager (mirrors managers/sms_manager.py)
• One-time config pass: prefix off, LF-only suffix, presentation mode
• Mount geometry — 10-15 deg window tilt, standoff, shroud — is ours to fix on the prototype
• Departs from the HID part named in project_objectives.txt — that doc needs updating

## Slide 6
Head to Head
Lighting Tolerance
• Camera: we tune exposure per site
• HID gun / Engine: fixed active illumination; engine adds our shroud
Unattended Integration
• Camera: CV pipeline + OS image we maintain
• HID gun: keystroke delivery + window-focus dependency
• Engine: one serial thread, nothing to focus
Control Over UX
• Camera: total, but all of it is ours to build
• HID gun: minimal — it just types
• Engine: trigger / beep / re-read delay set by scanning config codes
Cost & Roadmap Fit
• Camera: ~$35 BOM, the most dev work
• HID gun: ~$50-150; matches the objectives doc as written
• Engine: ~$25-70; needs a doc update + a small manager module

## Slide 7
Compatibility — session_manager.py
The Payload Is Scanner-Friendly
• 'sid:otp' = 23 ASCII bytes -> QR version 1 (21x21), ECC M: large, low-density, easy off a screen
• ':' is keyboard-layout-safe; re-scans are already idempotent (verify_otp returns 'already verified')
The One Gotcha
• verify_qr_payload() does payload.split(':', 1) with NO trimming
• A trailing '\r' -> otp = '123456\r' -> hash mismatch -> 'Incorrect OTP' AND burns a failed attempt
• Five such scans hit MAX_FAILED_ATTEMPTS and lock the session
The Fix
• Engine config: prefix off, suffix = LF only
• Reader glue: line.decode('ascii').strip() before verify_qr_payload()
• Optional hardening: payload.strip().split(':', 1) — also protects manual entry

## Slide 8
Recommendation
Prototype Now — Budget Engine (~$25-45)
• DYScan DE2120, Waveshare Barcode Scanner Module, or a GM65-class module
• Enough to prove the mount geometry, the serial reader, and the end-to-end pickup flow
Fleet — Decoded Engine: Zebra SE4710 / Honeywell N3680 (~$50-70)
• Noticeably better on dim, glary, or marginal screen reads — matters with no attendant to retry
• Same USB-CDC interface as the budget part, so swapping up is near-zero rework
Before Committing
• Bench read-reliability at min/max screen brightness, raking overhead light, bright backlight
• Reproduce the CRLF failure on purpose to validate the .strip() fix against real behavior
• Sign-off: update project_objectives.txt #7 / roadmap line 197 away from 'USB HID'