## Slide 1
Scanner Module:
Built, Then Refined
Scan-to-Print/Email/Wi-Fi (Phase 6) · Multi-Select, Preview & Copy Refinements
September 17-18, 2026

## Slide 2
From No Scanner to a Polished Pickup Flow
Session 1 built the scanner end to end -- hardware abstraction, capture UI, and a unified Wi-Fi/email pickup pathway. Session 2 went back over the result with a critical eye and fixed the rough edges a real user would actually hit.
Build
flatbed hardware -> capture UI -> print/Wi-Fi routing
Reconsider
debated splitting Wi-Fi vs. email, chose not to
Refine
multi-select, page preview, device-neutral copy

## Slide 3
Session 1 -- How It Works
scanimage -d <device> --format=png
shells out to sane-airscan, same pattern as lp/lpstat for CUPS
SaneAirscanScanner / SimScanner
managers/scanner.py -- real hardware or canned SIM_MODE pages
ScannerManager.finish()
combines captured pages into one PDF via fitz
scan_destination: Print Now / Send via Wi-Fi
the actual product decision from the objectives doc
ScanAdapter.handle_scan()
creates a source="scan" SessionManager session
scan_result (QR + OTP) -> phone -> /redeem
user's own phone downloads or emails the file
Print Now reuses the existing printing_options -> payment pipeline completely unchanged.

## Slide 4
Session 1 -- What Was Built
Hardware Abstraction
• ScannerInterface / SaneAirscanScanner / SimScanner (managers/scanner.py)
• Shells to scanimage CLI -- no python-sane binding needed
• SimScanner seeds canned pages, same seed-once idea as SIM_USB_DIR
Capture UI Rewrite
• screens/scanner: page counter, thumbnail, Scan/Rescan/Done/Cancel
• _scan_completed guard stops on_leave() from deleting a successful scan
• Old UI-only "DEV BYPASS" fake-scan path removed entirely
Print Routing
• scan_destination "Print Now" reuses file_browser's exact 3-arg handoff
• Zero downstream changes -- printing_options re-derives everything from the PDF
Wi-Fi/Email Pickup, Unified
• Reused the intake OTP/QR pattern in reverse instead of building a keyboard
• New GET/POST /redeem portal; verify_otp reused via its already-verified short-circuit
• /redeem/download and /redeem/email both live on the user's own phone, not the kiosk

## Slide 5
Session 2 -- How It Works Now
scan_destination: DestinationOption toggle(s)
Print Now and Download/Email are now independently selectable
Continue button (enabled once >=1 picked)
confirm_selection(selected_keys) replaces exclusive click-to-act
send_wifi selected? -> session created immediately
free, untied to payment -- unchanged behavior
scan_result
"Continue to Print" if a print was also requested, else "Done"
Continue to Print -> printing_options -> payment
pending_print hand-off carries the PDF + page list forward
No changes to SessionManager, ScanAdapter, or the /redeem router -- the combined pickup stayed as-is.

## Slide 6
Session 2 -- What Was Built
Multi-Select Destinations
• New DestinationOption(QFrame) wrapper around the shared Card widget
• Kept Card itself untouched -- every other screen depends on its one-shot click
• Both Print Now and Download/Email can be picked together, then Continue
Page-Thumbnail Preview
• New ThumbnailRenderThread (screens/scan_destination/thumbnail_thread.py)
• Renders the composed PDF via fitz, off the main thread -- mirrors file_browser's pattern
• Works automatically for SIM_MODE's placeholder pages, no extra path needed
Conditional "Continue to Print"
• scan_result gained pending_print + has_pending_print()
• Done button relabels and routes into printing_options when a print is also queued
• Temp PDF cleanup moved to whichever leg actually finishes last
Clearer, Device-Neutral Copy
• "Send via Wi-Fi" retitled to "Download or Email" -- both options now named in bold
• "your phone" replaced with "your own device -- phone, tablet, or laptop" throughout

## Slide 7
Tested and Working
115
automated tests passing offline, across both sessions (81 existing + 34 new in Session 1; no new unit-testable surface in Session 2 since SessionManager/ScanAdapter/redeem were untouched)
Covered Offline
• SimScanner, ScannerManager, SaneAirscanScanner error mapping
• ScanAdapter session creation (mirrors test_wifi_adapter.py)
• /redeem route tests, including download-then-email re-auth
• verify_otp_for_source_with_id success/failure cases
• flake8 clean on every touched file in both sessions
Needs the Real Thing
• Physical scanimage run against the HP Smart Tank 580
• Full phone-side /redeem download + email cycle against real SMTP
• Thumbnail strip's actual rendered output (compiles cleanly, not yet eyeballed)
• Multi-select combined path -- confirmed working via the user's own make run-sim pass

## Slide 8
What's Next
Hardware Validation
Run scanimage -L on the HP Smart Tank 580 to get the real SCANNER_DEVICE string, then validate one full scan-to-print and one scan-to-Wi-Fi cycle on actual kiosk hardware.
CLAUDE.md Refresh
Bring the doc current with Phases 2-6 together -- it still doesn't mention scan_destination/scan_result in the screen list or the scanner hardware row.
Visual Thumbnail Check
Confirm the scan_destination preview strip renders real page images at runtime, not just that it compiles and imports.
Temp-File Cleanup Scheduler
ScanAdapter's uploaded copies and ScannerManager's session directory are two independent temp-file sets with no expiry job yet.
Revisit the Wi-Fi/Email Split -- Carefully
If separate kiosk widgets resurface, the metadata/action-encoding design from Session 2 is a starting point, but re-litigate whether losing phone-side flexibility is worth it.
QR-Scanner Naming Collision
Reconcile project_objectives.txt / roadmap-planning.txt: the flatbed document scanner and the QR-pickup scanner are unrelated hardware, easily confused by name.