## Slide 1
Vouchers Done,
Real Money on the Kiosk
Voucher Completion · Kiosk Pi Bring-up · Payment Hardware
October 9 – 15, 2026 · Progress update, October 16, 2026

## Slide 2
From Simulator to Real Coins
The Voucher system was finished in SIM_MODE, then the app ran on the kiosk Pi for real: portal, screen and startup problems were fixed, the SD card was rebuilt, and real coins and change now work end to end. 12 PRs merged; tests went from 433 to 573.
Finish Vouchers
Apply, check balance, warn when change is low, report liability, read Voucher QR codes
Run on the Pi
portal loads offline, clean shutdown, UI scaled to 1080p, SD card rebuild guide
Real Payments
coins credit on the right pin, hoppers pay exact change, payouts fail safe

## Slide 3
Vouchers — How It Works
Low-change banner on idle / homepage
get_max_dispensable_change() < ₱20 threshold → warn, “Continue anyway?”
Shortfall at payout → VoucherManager.issue()
change the hoppers can't give becomes a V1:<code> Voucher
Customer returns: keypad or QR read
_on_qr_read → decide_qr_read → apply_voucher_code / check_voucher_code
transactions row
change_dispensed · voucher_issued · voucher_applied on the same row as revenue
Admin Dashboard /accounting
Change & Vouchers table + outstanding liability (unexpired remaining value)

## Slide 4
Vouchers — What Was Built
Apply at Payment + Balance Check (#53, #54, #56)
• On-screen keypad to type a code; Vouchers combine with cash or cover the whole job
• New voucher_balance screen from the homepage; one wrong-code lockout shared by both screens
Low-Change Warnings (#58, closes #24)
• Banner on idle/homepage below ₱20 of dispensable change; re-checked on every screen entry
• Idle asks “Continue anyway / Cancel”; payment says ungiven change becomes a Voucher
Dashboard Liability (#60, closes #28 — last child of #21)
• Change dispensed, issued, Applied summed from transactions so they reconcile with revenue
• Liability read from vouchers as of now; failed-print gap filed as #59
Voucher QR Reads (#61, #62, closes #57, #37)
• V1: reads Apply at payment, check on balance screen — verified on the Pi with the real reader
• Dispatch seam now tested (branch swap fails 3 tests); renamed to decide_qr_read

## Slide 5
Kiosk Pi — Phone to Portal
Phone joins the kiosk Hotspot
OS sends its “am I online?” probe
dnsmasq + nft (#63, open)
every name → the Pi; port 80 → probe responder on :8080; 443 reset
webapp/captive.py probe responder
not yet released → 302 /upload, so the OS opens its sign-in window there
Portal /upload (#50)
inline SVG icons, no internet fetches; other traffic rejected at once, not dropped
Captive-probe detection is ADR 0008, proposed; merge waits on the device test matrix.

## Slide 6
Kiosk Pi — What Was Built
Portal Works Offline (#50) + Clean Shutdown (#51)
• Font Awesome CDN replaced by inline SVGs; firewall rejects instead of drops
• Ctrl+C / SIGTERM now run cleanup() — needed for systemd stop later
UI Scaled to the Screen (#65) + make run over SSH (#67)
• UI_SCALE auto = height ÷ 800 → 1.35× on 1080p; all 16 screens fit, verified on the kiosk
• make run uses DISPLAY=:0 if the kiosk screen is up, otherwise headless
No pigpio = No Start (#66, open)
• Sim coin buttons appeared whenever pigpio failed to import — free credit on a real kiosk
• Now: SIM_MODE off + no pigpiod → log GPIO error and exit; sim buttons only in SIM_MODE
SD Card Died 2026-10-14 → Rebuild Guide (#69)
• docs/KIOSK_PI_SETUP.md: 17 steps from a blank card, with a done/not-done status table
• Printer, QR reader, autostart and Tailscale still to do on the new card

## Slide 7
Payments — Coin In, Change Out
Coin acceptor → GPIO 12 (#68)
5 ms glitch filter; count low pulses 10–150 ms wide
Pulse count → coin value
₱1 3–4 · ₱5 5–6 · ₱10 8–9 · ₱20 11–12; unmatched counts are logged
PaymentModel (signals connected once)
each coin credited once; money restarts the 60 s timeout
Hoppers: sensors GPIO 9 / 26 (#70)
motor off first; one 1.5 s attempt per coin, one 20–300 ms pulse
Coin not seen → stop that hopper
rest of the change becomes a Voucher; screen locked until payout ends

## Slide 8
Payments — What Was Built
Coins Credit (#68)
• Code listened on GPIO 17; acceptor is on 12 — pins now read from .env
• ~85 noise spikes/s filtered; pulse table fixed (₱1 was being ignored, ₱20 read as ₱10)
Hoppers Pay Exact Change (#70)
• Paid ₱11 for ₱4 and ₱75 for ₱14 — sensors were on 9/26, not 10/11 (found by scanning every GPIO)
• Blind runs capped: 1.5 s per coin instead of up to 50 s; a missed coin becomes a Voucher
Payout Safety (#70)
• Back and timeout can't cancel a paid job mid-payout; motors stopped at startup and on exit
• Fixes Ctrl+C leaving a motor running (31 coins out); enable pin set off before output mode
Double Credit Fixed (#68; also #64)
• Signals reconnected on every payment visit → Nth customer credited N×; now connected once
• #64 had the same fix but never merged; it can be closed

## Slide 9
Tested and Working
573
automated tests passing on main (433 at the start of the week, +140); flake8 clean
Covered Offline
• Voucher Apply, balance check, shared lockout, QR dispatch and order
• Dashboard change/Voucher figures reconcile with revenue; liability excludes expired
• Coin and hopper pulse filtering with synthetic pigpio edges, incl. tick wrap
• Payout lock: Back ignored mid-payout, timeout restarts on money
• UI scale resolution; portal has no outside URLs; hotspot rules in Docker
Verified on the Kiosk (Oct 15)
• ₱1/₱5/₱10/₱20 coins credit correctly, once each
• ₱10 for ₱6 → exactly ₱4; ₱20 for ₱6 → exactly ₱14
• Empty hopper → ~1.5 s run, Voucher covers the rest
• Ctrl+C mid-payout stops the motor; UI at 1.35× fits
• Still to test: bills (worn notes rejected), #63 devices, #66

## Slide 10
What's Next
Merge the pigpio check (#66)
Until it lands, a real kiosk without pigpiod shows sim buttons that add free credit.
Finish the new SD card
Printer, QR reader, systemd autostart and Tailscale, then back up the card image.
Retest bills with good notes
No bill was accepted on Oct 15 with worn notes; apply the coin-line filter if it still fails.
Captive portal device tests (#63)
Run the iPhone / Android / Windows / Mac matrix and decide HTTPS on the Hotspot (ADR 0008).
Close loose ends
Close #64 (shipped in #68); fix #59 so failed prints still reach accounting and coin inventory.
Remote access (#41)
Next on the roadmap: view-only Kiosk Admin in the Admin Dashboard over Tailscale.